ATEX roller door

- Individually ATEX-roller doors for hazardous areas.

- Available for zone 1/2 and 21/22.

- Combinable with requirements for sound insulation.

Door leaf:

The door leaf consists of double-walled, insulated steel slats, which are joined to a shell via a turnable connection system.

Execution as stainless steel roller door is possible.

The slats are produced individually, according to requirements of door and installation situation.

If additional soundproofing requirements are needed, the roller door will be executed with a soundproofing filling. To achieve high soundproofing values, the door leaf is covered with an acoustic hood.

Guide rail:

The guide rail consists of zinc-coated sheet steel in a screwed construction.

Drive:

Plug-on drive with built-in retainer or sprocket drive with separate retainer. In case of a power failure the door can be operated via an emergency crank. Opening and closing speed: appr. 0.2 m/s. Maintenance-free drive unit.

Control:

Control voltage 24 V, push button “Open-Stop-Close” on switch box, connection to on site socket on operating level.

Placement of drive and control inside or outside the ATEX-zone, depending on requirements.

Supplementary equipment:

- Surface coating: colouring according to RAL, DB, NCS

- Safety equipment: Omnidirectional and flash light, light barrier

- Control elements: push button "Open-Stop-Close", pull switch, key-operated switch, ex-prevented